## Slide 1: EE 277 Project Presentation May 13, 2021 Zoom Online
Group #02
Gaurav Deore
Nikhil Bellad
Keyur Doshi

## Slide 2: Project
Low Power Parallel to Serial Interface Using Asynchronous FIFO

## Slide 3: Outline:
Overview
Design Methodology
  Gray code pointer style #1
  Binary code pointer style
  Gray code pointer style #2
Design challenges & Learning outcome
Conclusion

## Slide 4: Overview:
Design and simulate a low power parallel to serial interface operating in two different clock domains capable of taking in parallel data converting it to serial data and transmitting it serially at the output appending start and end delimiters to the packet.

## Slide 5: Design methodology:
Parallel Interface
Async FIFO (Gray code pointer style #1)
Serial Interface

## Slide 6: Design methodology:
Parallel Interface
Async FIFO (Binary code pointer style)
Serial Interface

## Slide 7: Design methodology:
Parallel Interface
Async FIFO (Gray code pointer style #2)
Serial Interface

## Slide 8: Parallel interface:
Parallel Interface
P_clk
Test Bench
n_rst
parallel_data_in
grant
req
write_en
serial_data_out

## Slide 9: Parallel interface:
Parallel Interface is designed using FSM
It operates on two inputs request and grant
When the request and grant are high, the FSM moves to the input state where parallel interface starts getting the 32-bit data from the test bench.
After getting 32-bit input, FSM moves on to the output state where FSM send the 32-bit data serially to FIFO using counter and shift operation.
Once the 32 bits are completed FSM returns back to IDLE state.
Idle State
Rst = 0
Req = 0
Grant = 0
Input State
Rst = 1
Req = 1
Grant = 1
Output State
Sending 32-bit data to FIFO serially

## Slide 10: Parallel interface simulation results:

## Slide 11: Design methodology:
Parallel Interface
Async FIFO (Gray code pointer style #1)
Serial Interface

## Slide 12: Asynchronous FIFO:
Asynchronous FIFO’s are used in Clock Domain Crossing scenarios where the write clock is different from the read clock.
In this Parallel to Serial Interface, since the Parallel Interface and the Serial Interface work on different clocks, this FIFO is used to buffer the data .
Async FIFO (Gray code pointer style #1)
clk_in
full
dataOut
rst
flush
clk_out
insert
data_in
remove
empty

## Slide 13: FIFO Block Diagram:

## Slide 14: WRITE Module:
This FSM is used to write the data into the FIFO.
This block works on the parallel data clock.
The Insert signal is asserted to write the data.
This FSM checks for the full condition and writes data only when empty.

## Slide 15: Read Module:
This FSM is used to read the data from the FIFO.
This block works on the serial data clock.
The remove signal is asserted to read the data.
The FSM checks on the empty flag before it reads the data.

## Slide 16: Async fifo simulation results:

## Slide 17: Design methodology:
Parallel Interface
Async FIFO (Gray code pointer style #1)
Serial Interface

## Slide 18: serial interface:
Serial Interface
s_clk
output_psi
rst_n
req
data_in
pop
Reads data from the FIFO and outputs the serial data.
Handles the appending of delimiters.

## Slide 19: Serial interface simulation results:

## Slide 20: Putting all together:
SOD
DATA
EOD

## Slide 21: Synthesis Results:

## Slide 22: Synthesis Results:

## Slide 23: DESIGN Parallel IN and Seral out
Design Module PSI
Consist of Input state machine
asynchronous Fifo
Output state machine

## Slide 24: Design Modules
INput MODULE
COUNTER to count number of bits shifted to Fifo
Shift register
FSM
ASYSC FIFO
Dual port Memory module
Input p_clk and s_clk
OUTPut FSM
FSM

## Slide 25: Input State machine

## Slide 26: AsysC_Fifo

## Slide 27: Output state machine

## Slide 28: VCS Simulation results

## Slide 29: Power report

## Slide 30
AREA AND TIMING REPORT

## Slide 31: Draw back
Metastability issue can cause write pointer and read pointer FLAG false empty and full .
This can cause read_ptr to read memory location invalid data
Write pointer to overwrite valid data

## Slide 32: Parallel to serial interface using Asynchronous FIFO Design with Asynchronous Pointer Comparisons

## Slide 33: Sections of design
Top Wrapper
Parallel to serial Interface
FIFO module
Output logic
FIFO design
Dual port memory
Asynchronous comparator
Read pointer and empty flag
Write pointer and full flag

## Slide 34: Top Wrapper
The top wrapper connects all the top level design modules i.e parallel to serial interface, Fifo design and output logic.
The implementation of parallel to serial data is simple on the positive p_clk edge data is sampled and then it is given as output serially.
Push signal is used indicate valid data

## Slide 35: Fifo design
Fifo memory module: FIFO has input write clk, write data,write address ,read address, write increment.
Asynchronous Comparison: In this module uses comparison logic and asserts full and empty signal.
Read pointer and empty: This module controls read pointer empty signal it is in synchronous with read clock
The assertion of empty is asynchronous and depends on write pointer.
Write pointer and full: This module controls write pointer and full flag which is mostly synchronous with read clock but full signal is asserted when read pointer increments

## Slide 37: Direction set

## Slide 38: Direction clear

## Slide 39: Simulation Output

## Slide 40: Power output

## Slide 41: Area output

## Slide 42: Advantages and drawbacks
The implementation uses more number of flip-flops while reduces the
Combinational logic which is ideal for FPGA but may not be best for ASIC.
Due to reduction in combinational logic higher frequency can be achieved.
Extra efforts are required for STA due to asynchronous components.

## Slide 43: Design challenges & learning outcome:
Working with synchronizer circuit
Working with two different clock domains
Target cell library limitation during synthesis

## Slide 44: Conclusion:
Synchronization of FIFO pointers is safely accomplished using three different pointers technique in the cross clock domain.

## Slide 45: Reference:
C. E. Cummings, “Simulation and Synthesis Techniques for Asynchronous FIFO Design,” San Jose, CA, 2002. SNUG 2002 (Synopsys Users Group Conference, San Jose, CA, 2002) User Papers, March 2002, Section TB2, 3rd paper. Also available at www.sunburst-design.com/papers.
  [E-book] Available: http://www.sunburst-design.com/papers/CummingsSNUG2002SJ_FIFO1.pdf
Clifford E. Cummings and Peter Alfke, “Simulation and Synthesis Techniques for Asynchronous FIFO Design with Asynchronous Pointer Comparisons,” SNUG 2002 (Synopsys Users Group Conference, San Jose, CA, 2002) User Papers, March 2002, Section TB2, 3rd paper. Also available at www.sunburst-design.com/papers.
  [E-book] Available: http://discourse-production.oss-cn- shanghai.aliyuncs.com/original/3X/4/7/47fa3a7c83edfeea24029df12d0ae32f d9ed7610.pdf

## Slide 46
Thank you